MARS/HEFI System

Open MARS GUI and support windows on Monitor 3.

- Open WorkSpace menu and select MARS-HEFI>Start Mars-Hefi System.

The MARS GUI will appear as well as the MARS Camera Control used to take images

of the stack.  An SAOImage GUI also opens. Minimize this window.  And a MARS

GUI Pre-Alpha will appear. Minimize this window.

- The lower portion of the MARS GUI displays several ON/OFF buttons.  Locate the Wavescope

option and press the On button.  This must be turned on before the Wavescope software is brought online from the Frijole monitor.

- From the WorkSpace menu open “HEFI Light  Source” & “HEFI Interface”.  Both are found in

the MARS-HEFI submenu.

- Next press button #1 on KVM Switch panel located on equipment rack.  The Wavescope screen

should appear on the Frijole monitor.  If you do not see this press “Cntrl” and “~” simultaneously.

A blue screen menu will display a choice of computer screens to view. Select “Wave”.

From this screen double click on Wavescope icon.  This should bring up the software.

This concludes night time setup of MARS/HEFI System.