HET Opening Checklist

Ops Engineer:								Date:

Enclosure Thermal Control

- log into Jove as guider

- (3-3) open WXGui's & Netscape, check weather and AccuWeather swag

- update temperature in dome on smoke window to 2C less than SWAG.

System Checkout

- large air compressor: oil level, power on, test panel lights, start, check oil flow

- dryer: power on black button, then open large dryer valve slowly

- glycol startup: start, gauge at 8 GPM

- inspect interior: glycol drops, sweep pier, fan covers open, spectrograph room

- inspect exterior: glycol pump and tank, ahu's, chillers

- (1-1) open smoke: startwork

- (1-2) open SAMS Server and GUI, go to operate

- (2-1) open Dome GUI, open roof vents and home dome on GUI

- (2-2) open "LRS PXL Guider” as first of all guiders and check camera

- (2-3) open "HRS PXL Guider” and check camera

- (2-4) open “HRS Apogee Guider” and check camera

- (3-2) start MARS-HEFI system, turn Wavescope power on, open HEFI interface and HEFI light source GUIs via desktop pulldown menu

- open baffle xterm, check translation slide

- reset (Close, then reopen) SPS

- check calscreen

- open FIF/PMT GUI, home HRS and MOS probes, then watch HRS probe move to 242,000 and when done ensure lamps/camera are off (**while moving, click continue, not abort!)

- (4-1) open PMAC & Hexapod State Monitor, Crockett Tss, power up tracker, Tcs GUI

- enable structure, initialize, track, initialize search, test structure movement

- check weather: Mt Fowlkes & Locke GUI's, Netscape, visually

- open dome, CCAS shutter, louvers, roof vents; jcoff

- ensure unneeded lights around HET are off (i.e. loading bay, basement, GTAG)

- make sure dome lights are off, go to incandescents in the control room

(#-#) represents the Monitor and Screen used on Jove.

NOTES for TO:

# Text boxes

SWAG:___________________

Sunset Temp:______________

Dome Open:_______________

Truss Temp:________________

Outdoor Temp______________

Version 2004.5

29 Apr, 2004