HET OPERATIONS ENGINEER MANUAL:  TCS & TRACKER INITIALIZATION (REV:100204)

# TCS &TRACKER INITIALIZATION

PRECAUTIONS:

- The control room audio system should be set to monitor noise in the dome generated by the tracker.

General Description:

The following procedure will initialize the TCS and Tracker for night use.

Initial Conditions:

- Monitor 3, Screen 1  (3, 1) will display the Tracker Control System.

- The tracker is not initialized and is powered down i.e. the red lamp on the Tracker 3P Box (T3P box) is not lit.  The T3P box is located on the cabinet to the right of the Frijole monitor.

- Make an initial inspection that the tracker is near center .  If the tracker is positioned near any of its limits follow items 5.10 – 5.13 below.

- Start the Graphical  User Interface. Power up Tracker

  - From WorkSpace Menu select TCS-Crockett. (Note: To access WorkSpace Menu press the

right mouse button.

  - Open a PMAC State Monitor

  - Open  a Hexapod State Monitor

  - Open  a Tss – Crockett window.

- In this window type tss at prompt

ii.    Wait for instructions in Tss window  to power up tracker.

iii     On the cabinet, push the black button labeled “Tracker Power On”. The red light to

the  right should turn on, indicating that the tracker has power.  The red LEDs above

should all turn green. If the tracker light turns off see Fault Conditions and

Solutions.

iv      Now press enter in Tss-Crocket window.

d.     Open  TCS GUI from the WorkSpace Menu

All the positional data for the tracker will be displayed in the Tss-Crockett window.  Notice what the position numbers are for the upper and lower x, and y.  If the tracker is centered the numbers for upper and lower x should be around –3 and y should be around 75.

- Tracker Initialize Search.

  - An initialize search should be completed on the tracker to ensure full confidence that the tracker knows its position before beginning night operations.  Go to the interface and click on the TOOLS menu.  Choose ‘TRACKER POSITION’.  A small window will appear showing the trackers current position.  Click on the OK button at the bottom.

  - A new window will appear asking you too either select TRACK, SLEW, or CANCEL.  Select TRACK.  The tracker motors for tracking will now be enabled.  This can be verified by checking the PMAC State Monitor shell.  The track motors will have ‘enabled’ next to them.

  - Now go back to the TOOLS menu and select ‘INITIALIZE TRACKER…’.

  - A small window will appear.  Select INITIALIZE SEARCH. The tracker will now go through and find accurate positions for the hexapods, y, rho, and upper and lower x.

  - The ‘initialize search’ process will take about ten minutes to complete.  During the process use the video monitor and the various positions of the audio system microphones to discern correct movement, and sounds that may indicate a mechanical problem.

  - Once the process is complete the upper and lower x should be at a position of around 24 with both upper and lower x position numbers matching, and y should be located at 157.

  - There should be green lights next to each item on the small ‘tracker initialization’ window.  Close this window out.   and click the red ‘abort’ button on the interface.  This command stops the motors and sets the brakes.  Once again use the PMAC State Monitor shell to confirm that the brakes are set.

  - Do not click on the ‘red abort’ button until the upper and lower x are reading the same position number.  Even if a ‘green board’ has been received indicating that the initialize search process is completed, the upper and lower x are still going through the process and the numbers have not settled down to indicate the same position for both the upper and lower x.

  - Once the upper and lower x position numbers are the same click on the ‘red abort’ button on the TCS interface.  This command stops the motors and sets the brakes. Once again use the PMAC State Monitor shell to confirm that the brakes are set. The tracker is now ready to commence night operations.

  - If the tracker has been left up near the limits from previous operations, the tracker will have to be moved a small distance before an initialize search can be completed.  Otherwise during the initialization process the tracker would be driven up into the limits and the search would not be completed.

  - As an example lets say the tracker is at the upper right position which yields an upper and lower x position of around 1598 and a y position of around 1629.

  - After step 2.10 above go to the TOOLS menu and select tracker position.  Enter x and y positions of 1400.  Then chose either TRACK or SLEW to move the tracker to the position selected.

  - Now an initialize search can be completed without driving the tracker up into the limits.

Fault Conditions and Solutions:

- The red light on the T3P box does not stay lit after pressing ‘enter’ and the tracker does not power

up.  Also, the PMAC State Monitor shell will display ‘page is not updating’ message.

  - Exit crockett then repeat steps outlined in section 3.0 until tracker powers up.

- ‘SKEW LIMIT SWITCH TRIGGERED!!! STOP!!!’ message is displayed in the PMAC State

Monitor shell and the tracker will not power up.

  - Check to see if an emergency stop button has been pushed by looking at the display on the

rack to the right.  If an emergency stop button has been pushed a red light will be lit next to

the location.

  - Discern why the button was pushed and make sure the situation is resolved.  Make sure the

button that was pushed is in the out position and then repeat steps in section 3.0 above.

  - If an emergency stop button was not pushed check the upper and lower x values to make

sure they are not different by more than 15 mm.  If they are wait for the TO to arrive

before continuing.

4)    If an emergency stop button has not been pushed and item 3 above is not the case then

check the glycol control box for an EF5 fault.  An EF5 is an external power fault. If an EF5

fault has occurred push the reset button on the box and then restart the unit.  Check the

glycol flow gauge on the equipment rack in the control room for flow rate.

5)   If 1-4 above have not occurred then exit and restart crockett until tracker stays powered up.

a)  Put the cursor within the crockett shell and press the ‘backspace’ key.  Type ‘exit’ and

press ‘enter’.  Repeat steps as outlined in section 1.0 above to power tacker up.

- If the TCS interface is up when the skew limit switch error occurs, then do the following.

  - Go to the TOOLS menu and select TRACKER SHUTDOWN.

  - Then go back to the TOOLS menu and select RELINQUISH CONTROL OF THE TRACKER.

  - Once again under the TOOLS menu disable the structure.

  - Select the file menu and exit the TCS interface.

  - Place the cursor in the crockett shell, do a ‘backspace’ followed by typing ‘exit’ at the crockett prompt and press ‘enter.  This exits the crockett software.

  - Now repeat steps as outline in 1.0 above to bring crockett back up.

C)  Core Dump Error.

1)   If a core dump fault has occurred the tracker will not power up and the error message

‘GATFloating exception (core dumped)’ will be displayed on crockett.

2)   To clear the error, exit to the main prompt by doing a backspace and then typing exit in

crockett.

3)   At the prompt type ‘pe xy’ and press ‘enter’.

4)   At the pe xy prompt that appears type ‘$$$’ and press ‘enter’.

5)   Do a ‘Ctrl D’ to exit the utility.

6)   Power up the tracker as outlined in section 3 above.

D)  Either an XY or a Rho fault is displayed on the TCS GUI.

1)   Reset the appropriate amp on the T3P box by toggling the switch.

2)   Click on the red ‘ABORT MOVE’ button on the TCS GUI.

3)   The fault should clear.  If not, repeat 1 and 2.

4)   If the rho fault occurs again the PFIP should be checked to make sure there is nothing

hindering movement of the rho stage.

Method for System Shutdown:

- The method is as outline in B).6), items a) thru e) above, with the following additions.

  - After TRACKER SHUTDOWN is selected from the TOOLS menu an alarm will sound from the equipment rack.  Wait until this alarm has quit sounding before going to the next step and selecting RELINQUISH CONTROL OF THE TRACKER.

  - Once the crockett software has been exited, put the cursor in the TCS background and left click.  A menu will appear; select exit from it.  Then left click ‘OK’.  This action will exit the TCS software, and concludes the system shutdown method.

Special Tracker Procedures:

- Instructions for Manually Controlling the Tracker Rho Brake.

  - Discussion:  The rho brake system is a magnetically held mechanism.  Magnets and springs hold the brake open or closed to avoid heat dissipation on a solenoid system.  Therefore there are two PMAC variables that control the rho brake: M40, which controls the state of the brake, and M41 which controls the ‘pull’ mechanism that will pull the brake to release it.  The pull mechanism is a solenoid type device.  The sequence to release the brake is to release the brake mechanism (M40=1), then activate the pull mechanism for 1 second (M41=1), then deactivate the pull mechanism (M40=0), and finally set the brake mechanism (M40=0).  The activation time for the pull mechanism is not rigid to avoid heat dissipation.

In addition to controlling the brake the safety plc, plc30, must also be shutdown.  Plc30 monitors the state of the motors and the brakes.  Anytime it sees a motor off, the plc commands the associated brake to set.  Plc30 is primarily to prevent back drive on the Y axis.  Make sure that plc30 is enabled when the procedure for controlling the rho brake is finished.

  - Points to watch out for:

    - The first character that is typed at tss will cause the cursor to move to the command line.  The second character will start the command buffer.  Make sure the command gets entered correctly.

    - Be aware of the position and status of the rho stage.  Don’t release the brake if the stage is out of balance and there is a chance that the stage could swing down.

    - Verify that the command is correct before sending it.  It is very easy to type the wrong M variable number and change something you don’t want to change.

  - Procedure for controlling the rho brake.

    - On the crockett shell start tss, if the program is not already running, by typing

‘tss’ at the prompt.  Do not start TCS.

    - At the crockett prompt type “xy displc30” and press ‘enter’.

    - Now release the brake.  At the prompt enter the command “xy m40=1m41=1”, then enter the command “xy m41=0.

    - To set the brake enter the command at the crockett prompt “xy m40=0”.

    - To shutdown enable plc30 by entering the command “xy enaplc30”.

    - This concludes the rho brake procedure.