HET OPERATIONS ENGINEER MANUAL:  SAMS STARTUP AND CALSCREEN CHECK (REV08.08.04)

# SAMS STARTUP

General Description:

Startup the SAMS software

- Start SAMS Server.

  - Place the cursor in the left most monitor, second screen,  then press and hold down the right mouse button.

  - A menu will appear.   Select ‘SAMS’ from the menu; then from the submenu select ‘Start SAMS Server - Gap’ and release the right mouse button.  A shell will appear.

  - Labview will start, and in turn, automatically start and run SAMS Server .

  - Watch the status bar at the bottom of the SAMS Server interface until the message “Running Main Application Loop” appears.

  - Go back to the Jove menu and select ‘Start SAMS GUI’   The SAMS GUI interface will appear.

  - From SAMs GUI select “Operate” from Change Mode This concludes the SAMS

software startup.

Fault Conditions and Solutions:

metric is steadily growing

PMCS new combo and both PMCS and TSPS busy lights show constant orange

SPS out of memory (see SPS section)

SAMS/PMC loop not cycling

check .ttp values in SAMS

if sams sending all zeros & 7 sec from get ttp to ttp done

the needed correction size may exceed the max setting

try opening the max move size a bit

if sending all zeros, & 1 sec ... ? dunno

metric exceedingly large

check edge sensor data

if entire bank (see mirror diagram) gives values of -384.00

open SPS/SAMS loop (select all no's in PMUI - SAMS Gui)

quit/close all SAMS software

power cycle brick (in UER)

check MTM master timing module in igloo (goes to brick in UER)

3 channels - all hould be pulsed, not steady

if problem persists a hub board may be bad - SAMS deadlined

bring SAMS software back up

reclose SPS/SAMS loop

sensor reported bad

open loop

return to standby

remove in SAMS

back to operate

wait a few minutes

check for error msg's

if none

reclose loop

SAMS

??? server halted (when starting labview)

~10 minutes did not elapse since old version of SAMS was closed.

wait and retry.